## Slide 1: Impact-based ensemble forecasting of tropical cyclones
Yohei Sawada
The University of Tokyo
Special thanks to:
Le Duc, Futo Tomizawa, Mai Hung, Yuki Hirose, Kazuo Saito, Md. Rezuanul Islam

## Slide 2: 1. Introduction

## Slide 3: 1.1. Ensemble forecasting opens the door to impact-based forecasting
JMA’s Mesoscale ensemble prediction system
(MEPS)
truth
prediction
Sensitivity -> hard to predict severe events
truth
prediction

## Slide 4: 1.2. “Huge” ensemble forecasting: forefront of the NWP science
[Duc et al. 2021 SOLA https://doi.org/10.2151/sola.2021-007]
1000-member ensemble forecast by Fugaku supercomputer
[Kobayashi et al. 2020 NHESS https://doi.org/10.5194/nhess-20-755-2020]
Put them to river model
“Huge” ensemble impact forecasting

## Slide 5: 1.3.1. Challenges in ensemble forecasting toward impact-based forecasting (1)
Are you using ensemble data operationally?
Orange：Regularly use, Red：Not available but would like to have, Blue：Not available or required
More impact-based
[Titley et al. 2019 Tropical Cyclone Research and Review
https://doi.org/10.1016/j.tcrr.2019.10.005]

## Slide 6: 1.3.2. Challenges in ensemble forecasting toward impact-based forecasting (2)
How to generate “good” ensemble by explicitly considering all the relevant uncertainties in an efficient way?
How to effectively use ensemble in an operational timeframe?
Scenario analysis?
All the ensemble could not capture observation very well…
ensemble mean?
Challenge 1
Challenge 2

## Slide 7: 2. Challenge 1: quantifying all the relevant uncertainties in ensemble forecasting

## Slide 8: 2.1. Goals
Dynamic Core
Selection of parameterization
Function call
Cumulus
Op.1
Op.2
Op.3
Cloud
Op.1
Op.2
Op.3
Radiation
Op.1
Op.2
Op.3
…
Para. 1
Para. 2
Para. 3
Selection of parameters
Atm. Model
Current
state
Future
State
We would like to get ensemble of selected parameterization and parameters based on observation efficiently and objectively to quantify all relevant uncertainties.
Observation data
Probabilistic!
Deterministic or expert knowledge….

## Slide 9: 2.2.1. Key ideas (1): Blended parameterization
Blended Model
Dyn. Core
Cloud
Op.1
Op.2
Op.3
Dyn. Core
Cloud
Op.1
Op.2
Op.3
[Mai et al. 2020 HESS]
or
or
Instead of choosing a scheme, we call all schemes to calculate weighted mean of increment of state variables. Then, we optimize weights as parameters
 We can simultaneously solve scheme selection and parameter optimization as optimization problem of continuous variables.
 It is expected to increase model performances by integrating several schemes.
Parameters！

## Slide 10: 2.2.2. Key ideas (2): Efficient parameter optimization with machine learning
Global Sensitivity Analysis
Machine learning-based surrogate model
Evaluate the sensitivity of parameters to observation
 Focusing only on sensitive parameters!
Parameters
Dynamic model
Output
Statistical model
Accelerate the iterative processes of parameter optimization.
Bayesian inference
[Dong et al. 2019]
Although we must iteratively evaluate model parameters, we can avoid running an atmospheric model using machine learning based surrogate models.

## Slide 11: 2.3.1. Case study 1: 2015 Typhoon Kilo and Etau
[Ushiyama et al. 2017]
In 2015, more than 600mm rainfall hits Kanto and Tohoku regions due to quasi-linear rainband induced by two tropical cyclones.
The levee collapsed in Kinu river affecting a number of people.
Atmospheric model: WRF [Scamarock et al. 2008] Enabling 33 parameters to be optimized, which include the selection of parametrizations. Parameters are optimized by radar-based rainfall.
River inundation model: RRI [Sayama et al. 2012]
Evaluating the skill to forecast river discharge.

## Slide 12: 2.3.2. Parameter optimization.
Optimization results of 8 sensitive parameters (from total 33 parameters)
Red: Truth, Blue: Posterior probability density
(This is an idealized experiment)
[Tomizawa et al. in prep]
We can effectively constrain sensitive parameters by our method.
But large uncertainty remains (i.e. observation could not perfectly determine parameters).
Ensemble that samples this uncertainty is really necessary!

## Slide 13: 2.3.3. Rainfall prediction
time
0h
24h
present
Training period
36h
Rainfall RMSE against Radar-AMDAS
Rainfall RMSE against Radar-AMDAS
Our optimized parameter improves future rainfall simulation!
[Tomizawa et al. in prep]

## Slide 14: 2.3.4. Flood prediction
Our optimized parameter improves future river discharge simulation!
 All optimization process can be done less than 2-hour. Our proposed ensemble generation is computationally feasible.
River discharge simulation at Kinu river
present
present
[Tomizawa et al. in prep]

## Slide 15: 2.4.1. Case study 2: Multi-physics Ensemble prediction in Viet Nam
Application to Viet Nam Operational Ensemble prediction system
Viet Nam has already operated the 32-member ensemble prediction system in which each member choose 1 from 25 = 32 combination of parameterization from 5 physics component.
 “Blended” parameterization is applied and optimized by rainfall observation.

## Slide 16: 2.4.2. Case study 2: Preliminary results
Dyn. Core
Cloud
Op.1
Op.2
Op.3
Dyn. Core
Cloud
Op.1
Op.2
Op.3
Ensemble mean rainfall
Ensemble mean rainfall
Our new 32-member system eliminates the spurious rainfall. In addition, we can get a larger spread of rainfall forecasting, which potentially reduces the probability to fail strong rainfall.

## Slide 17: 3. Challenge 2 (PART I): Is ensemble mean beneficial?

## Slide 18: 3.1. Value of ensemble mean prediction
Radar-observed rainfall
JMA’s deterministic
JMA’s ensemble mean
Ensemble mean is one of the reasonable choices to represent ensemble members.
But.. For many relevant variables to impact-based forecasting, ensemble mean is useless (in the case of small ensemble sizes)
[Duc and Sawada 2024 JMSJ]

## Slide 19: 3.2. Why is ensemble mean of precipitation so bad?
Consider 1-D world, and there are two ensemble members of rainfall distribution (Green)
Let’s identify the “center” of these two members.
Ensemble mean suggests the blue line as a center, which is something wrong….
1-D world
We could not get the red line as a center of two members when using arithmetic mean.
Can we define another “mean” to get red line?

## Slide 20: 3.3. Key idea: Using optimal transport theory
To obtain “center”, we implicitly define “distance”.
We should change the definition of “distance”.
Sum of difference in pixel by pixel gives us “distance”.
“Distance” in arithmetic mean
The cost of moving one data to the other give us “distance”.
 Wasserstein distance
“Distance” in optimal transport theory

## Slide 21: 3.4. New mean based on “Wasserstein distance”
JMA operation mesoscale ensemble prediction
Deterministic
ensemble mean
“new” Ensemble mean
New “mean” does not destroy the coherent structure of rainfall in longer lead-time, so that they can get better skill score.
 You can use single “mean” of ensemble forecast!

## Slide 22: 4. Challenge 2 (PART II): Advanced scenario analysis by ensemble forecasting of tropical cyclones

## Slide 23: 4.1. Do you want the “worst-case scenatio”?
Let’s assume two port cities, A and B
A
B
Ensemble prediction
Alart！
Alart！
[NOAA NHC https://www.nhc.noaa.gov/experimental/inundation/]
Note that the worst-cases for A and B never happens at the same time!
To consider large-scale (or nationwide) operation for pre and post disaster management, more realistic worst cases are required.
Combining worst-case for each point

## Slide 24: 4.2. Key idea: Pareto frontier analysis
Storm surge hazard in B
Storm surge hazard in A
S
t
S is Pareto dominant to t
(s is severe in both A and B)
u
S is not Pareto dominant to u
(s is severe in B but not in A)
Ensemble members are plotted in 2-D graph according to their storm surge hazard
Pareto frontier
= Set that we should check as the worst case.

## Slide 25: 4.3. Case study
2019 TC Hagibis
Combining meteorological and storm surge model, surge height is simulated by 1000 ensembles
Atmospheric model: JMA-NHM [Saito et al. 2006]
Ensemble method: EnVAR [Duc et al. 2021]
Storm surge model: SSHPI [Islam et al. 2021]

## Slide 26: 4.4. Pareto frontier of storm surge risk in Tokyo bay
Surge height in 4 points in Tokyo
Red: Pareto frontier of highest cases
Blue: Pareto frontier of lowest cases
Track forecast
White : ensemble mean
Red: Pareto frontier of highest cases
Blue: Pareto frontier of lowest cases
 We successfully get 4 “realistic” worst scenario from 1000 members

## Slide 27: 4.5. Pareto frontier of storm surge risk in Tokyo bay
Composite analysis of wind field
Left: Pareto frontier of highest cases
Blue: Pareto frontier of lowest cases
landfall
-12h
-24h

## Slide 28: 5. Summary
How to generate “good” ensemble by explicitly considering all the relevant uncertainties in an efficient way?
 It is possible to explicitly consider parametric and model selection uncertainties for better ensemble generation.
How to effectively use ensemble in an operational timeframe?
We can use ensemble “mean” under new definition of distance.
Pareto optimality is useful to extract realistic worst-case scenario from large ensemble data
Scenario analysis?
All the ensemble could not capture observation very well…
ensemble mean?
Challenge 1
Challenge 2

## Slide 29: 6. Sawada Group at the University of Tokyo (Department of Civil Engineering)
“Mathematical Hydrological Disaster Science Group”
Yohei Sawada
Associate Professor
Le Duc
Assistant Professor
https://sites.google.com/view/sawadaresearchgroup/home
Any collaborations are highly welcome!

## Slide 30: 7. Japan’s new program to discuss the controllability of tropical cyclones
https://spectrum.ieee.org/weather-control-japan-moonshot
Japanese government launched the new R&D program to pursue weather controllability. This program includes many other social issues, such as international agreement.
Any comments/collaborations are welcome!