## Slide 1: Multi-layered Water-related Disaster Risk Reduction toward Early Warning for All
KIKUTA Tomoya
Director for International Coordination of River Engineering,
Water and Disaster Management Bureau
Ministry of Land, Infrastructure, Transport and Tourism (MLIT), Japan
November 30, 2023
ESCAP/WMO TYPHOON COMMITTEE
18th Integrated Workshop / 4th TRCG FORUM
TECHNICAL PRESENTATIONS (PLENARY)
- Japan-

## Slide 2: TOC of Today’s Presentation
EWS for flood risk reduction in Japan [EWS in Japan]
Application to municipality governance [EWS for Local Government]
Application to efficient dam control [EWS for dam operation]
International contribution by Japan
Multi-layered Water-related Disaster Risk Reduction toward Early Warning for All
- Japan-

## Slide 3: TOC of Today’s Presentation
EWS for flood risk reduction in Japan [EWS in Japan]
Application to municipality governance [EWS for Local Government]
Application to efficient dam control [EWS for dam operation]
International contribution by Japan
Multi-layered Water-related Disaster Risk Reduction toward Early Warning for All
- Japan-

## Slide 4
Hydrological observatory network in Japan
Radar rainfall observatory
Relay station
Regional Development Bureau
Warning board
Meteorological Observatory
Ground rainfall observatory
Water level / discharge observatory
Disaster Management office
catch of gauge
flow of rain water
tipping bucket
outlet
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 5
Hydrological observatory network in Japan
Administrator | Rain gauge station | Water gauge station
River and disaster management bureau, MLIT | 3,490 | 1,934
Japan Meteorological Agency | 1,302 | －
Prefectures | 5,189 | 4,634
Total | 8,691 | 6,568
Number of observation posts distributing data via automatic data transfer units (as of Mar. 2018)
Type | Frequency
Ground rainfall observation | ▪ hourly ▪ 10 min (flood time, etc.)
Rader rainfall observation | ▪ C-band：5 min to 10 min ▪ X-band：1 min to 2 min
Water level observation | ▪ hourly ▪ 10 min (flood time, etc.)
Discharge observation | ▪ Low flow measurement: 36+ times / yr ▪ Flood flow measurement: 10 floods / yr
Frequency of observations
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 6
Flood risk information
Municipality View
Prefecture View
Forecasts and warnings are issued in response to changes in water level, and the color of the river displayed will also change.
Click on the camera icon to check a live image showing the current condition of the river.
Learn the current rainfall status from radar.
Learn the current state of river water levels and rainfall.
Camera Image
Red: Flood Risk Information Issued
Orange: Flood Warning Information Issued
Yellow: Flood Warning Issued
Ibaraki Pref.
Tochigi Pref.
Watarase River
Tsukubamirai City Hall
Torede
Toride City Hall
Tone River
Bandai Bridge
Live Camera
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 7
Flood risk information
River Water Level Legend | 
Flood Danger Level | Level at which there is a danger of river flooding
Evacuation Decision Level | Level which provides the basis for issuing an evacuation order
Flood Warning Level | Level at which caution should be exercised for the river flooding
Flood Fighters Alert Level | Level at which flood fighters are placed on stand-by
Understand the current risk of flooding based on the river water level.
When the river water level is rising, the mark (rising) will be displayed together with the water level information.
The higher the water level of nearby rivers, the greater the likelihood of flooding in your area.
For nearby rivers with a high risk of flooding, please ensure that you are safe and take appropriate disaster prevention action.
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 8: TOC of Today’s Presentation
EWS for flood risk reduction in Japan [EWS in Japan]
Application to municipality governance [EWS for Local Government]
Application to efficient dam control [EWS for dam operation]
International contribution by Japan
Multi-layered Water-related Disaster Risk Reduction toward Early Warning for All
- Japan-

## Slide 9
Integrated Water-Related Disaster Information System for Municipalities (IDR4M)
Problems at municipalities
Limited officials and lack of experience for disaster response
Huge amount of disaster related information to check in a short amount of time
IDR4M aims to provide disaster risk information to municipalities for science-based decision-making in disaster response operations, such as issuing evacuation order
Clear Evaluation Criteria (e.g. Water level, Rainfall amount
Unclear Evaluation Criteria (e.g. degree of hazard concerning flooding and Mud-flow)
Using AI tech for Analysys
Mayor Decision
(e.g. Evacuation order)
Integrated-System of Disaster Reduction for Municipalities (IDR4M)
Evacuation Action
Huge amount of Disaster Information
Hazards, Vulnerabilities, etc
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 10
Integrated Water-Related Disaster Information System for Municipalities (IDR4M)
1) Integrate disaster information and deliver them to municipalities in a usable manner,
2) Develop an integrated hazards/vulnerabilities risk information system, and
3) Provide real-time/pinpoint risk information to residents.
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 11
Integrated Water-Related Disaster Information System for Municipalities (IDR4M)
【Usage example: IDR4M Disaster risk of Katori city
affected by Typhoon No.8, on August 8, 2021】
Legend: Disaster risk
Evacuation（Evacuation Instruction）
Preparation（Evacuation of the Elderly, Etc）
Advisory
9:10 Disaster risk forecast after 4 hours; 13:10
13:40 Disaster risk forecast after 3 hours; 16:40
July 2021
August
2021
Sept. 2021
July 2022
Sept. 2022
13:36 issued
“Heavy rain warning”
14:50 issued “Evacuation of the elderly, etc”
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 12
Integrated Water-Related Disaster Information System for Municipalities (IDR4M)
Obihiro City, Shintoku Town, Sikaoi Town and Memuro Town, Hokkaido
Selected 18 municipalities from whole Japan in terms of different topography and characteristics.
Conducted demonstration experiment in the model municipalities.
Maizuru City, Kyoto
Ngaoka Citym Niigata
Kakogawa City, Hyogo
Takahashi City, Okayama
Toho Village, Fukuoka
Katori Citym Chiba
Himi City, Toyama
Adachi Ward, Tokyo
Fujikawaguchiko Town, Yamanashi
Tochigi City, Tochigi
Takamatsu City, Kagawa
Joso Citym Ibaraki
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 13: TOC of Today’s Presentation
EWS for flood risk reduction in Japan [EWS in Japan]
Application to municipality governance [EWS for Local Government]
Application to efficient dam control [EWS for dam operation]
International contribution by Japan
Multi-layered Water-related Disaster Risk Reduction toward Early Warning for All
- Japan-

## Slide 14
Long-term rainfall prediction and decision support system for the Integrated dam operation
Handling uncertainty contained in the predictions has been issues.
Normal period
Before a flood event
After the flood event
Overestimated prediction
Pre-release
Before a flood event
After the flood event
Insufficient water recovery
Inflow less than predicted
No pre-release
Risk of overflow
Inflow more than predicted
Underestimated prediction
Nohara 2020
It is difficult to know suitable amount of preliminary release volume because of rainfall prediction uncertainty.
Flood risk reduction
Secure stable water supply,
Renewable energy
Tradeoff on dam operation
SIP Model
Cross-ministerial Strategic Innovation Promotion Program
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 15
Long-term rainfall prediction and decision support system for the Integrated dam operation
EWS for dam operation
②Ensemble rainfall prediction
⑦Integrated Operation of Reservoir Systems
①Ensemble prediction of typhoon track
Rainfall-Runoff Modelling
GSM（84hrs）
③Ensemble rainfall prediction (51 ensemble)
④Ensemble inflow discharge (3 representatives)
⑤Ensemble accumulated storage volume (3 representatives)
⑥Optimization of dam flood mitigation operation
Ensemble High
Ensemble Mean
Ensemble Low
Ensemble High
Ensemble Mean
Ensemble Low
Ensemble High
Ensemble Mean
Ensemble Low
ECMWF, 51 Ensemble,
15 days advance, Downscaling 1km, 1hr
Prediction of necessary storage volume
DRO/EF Occur Level
ECMWF（15Days)
Triggered by Ensemble High but storage volume is defined by Ensemble Low for secure storage recovery.
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 16
Long-term rainfall prediction and decision support system for the Integrated dam operation
①Necessary storage volume for flood control
②Possible recovery storage volume
Ensemble High
Ensemble Low
Ensemble High: Mean value of No.1-5
Ensemble Low：Mean value of No.47-51
Accumulated rainfall (mm)
Rainfall Prediction in Reservoir Catchment Area
Dam Inflow Prediction
Ensemble High
Ensemble Low
Ensemble High
Ensemble Low
Necessary storage volume(×106m3)
Possible recovery volume(×106m3)
Detection of occurrence of DRO/EF （5 days before Typhoon landing）
Inflow excess flood control volume
Flood control volume
Target drawdown volume is increasing gradually keeping secure water recovery
SIP Ensemble pre-release operation (SIP-EPRO)
Using Long-term Ensemble rainfall prediction, optimum drawdown storage volume is obtained by adaptive pre-release under prediction uncertainty.
Balancing both flood and water security risks.
(Kido et. al. 2020)
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 17: TOC of Today’s Presentation
EWS for flood risk reduction in Japan [EWS in Japan]
Application to municipality governance [EWS for Local Government]
Application to efficient dam control [EWS for dam operation]
International contribution by Japan
Multi-layered Water-related Disaster Risk Reduction toward Early Warning for All
- Japan-

## Slide 18
Kumamoto Initiative for Water -Overview-
Solution of social issues
Sustainable economic growth
Enhancement of governance and systems
- Cooperation with the related organizations of each country and human resource development
- Cooperation with assistance organizations and international organizations
Use of observation/forecast data
Planning and operation of facilities
Sewerage systems
Reduction of inundation in urban areas / Use of sewage sludge for biomass power generation
Irrigation and drainage facilities
Reduction of flooding in rural areas by the use of the rainwater storage function of paddy fields
Reduction of greenhouse gas emissions through small hydroelectric power generation
Evaluation of water-related disaster risks
Effective use of existing dams
Operational improvement (operation rules)
Renewal (redevelopment) of dams
Preliminary release operation
Higher hydroelectric power generation efficiency
Enhancement of discharge facilities
Raising of the dam height
Climate change mitigation measures
Climate change adaptation measures
Development of “Quality Infrastructure” by the use of hybrid technology to implement both adaptation and mitigation measure
Satellite observation
Data integration & analysis
Risk map/Flood analysis
Support corporate investment and countries in which the measures are implemented
Creation of clean energy
Promotion of energy conservation
Reduction of greenhouse gas emissions
River basin sustainability and resilience against water-related disaster risks
Flooding of rivers
Inland flooding
Flooding in rural areas
1. Promoting both climate change adaptation and mitigation measures
2. Promotion of measures to improve people’s basic living environment
Local governments’ know-how and technologies
Use of IoT technologies
Ensuring access to safe water
Maintenance of sanitary environments
Water supply
Sanitation facilities
Expansion and updating of water supply facilities
Capacity building for the operation and management of the facilities
Forecast technology
Providing financial assistance worth approximately 500 billion yen over the next five years
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 19
EWS-related component of the Initiative
Use of observation/forecast data
Evaluation of water-related disaster risks
Satellite observation
Data integration & analysis
Risk map/Flood analysis
Support corporate investment and countries in which the measures are implemented
Forecast technology
MLIT of Japan proposes the “Flood Risk Mapping with Ground /Satellite Observation Data” as the new Annual Operation Plan No.6 [New AOP6] (2024-2027) under the Working Group of Hydrology [WGH] in ESCAP/WMO Typhoon Committee [TC].
Notes: Next, I would like to introduce the EARLY WARNING system in Japan.
In order to establish an early warning system, rainfall, water level, and flow rate observations are necessary.

## Slide 20
ありがとうございました。
Thank you for your kind attention.