## Slide 1: A Study of Typhoon Analysis using Wind Data of GK2A Satellite
Jinho Shin1, Hyun-Kyoung Lee1, Inchul Shin1, Ji-Hoon Jung1, Hee-Ae Kim3, Jun Dong Park2, Jung-Hoon Sohn1
1.National Meteorological Satellite Center, Korea Meteorological Administration (KMA),
2. National Aeronautics and Space Administration (NASA),
3. Seoul National University (SNU)
ESCAP/WMO TYPHOON COMMITTEE 18th Integrated Workshop/4th TRCG FORUM(23.11.27~12.1/Bangkok , Thailand)

## Slide 2: Why we need satellite observation?
Surface instruments are convenient to set up and operate, but they have difficulty in observing weather condition over ocean or upper atmosphere.
Satellites can provide information on ocean or the upper atmosphere for 24 hours with high resolution.

## Slide 3: Why to estimate sea surface winds from satellites?
Sea surface wind(SSW)s from scatterometer of low earth orbit(LEO) satellites are very useful for analyzing low-level winds in oceans and typhoon wind radii(>15m/s). But hey are limited to data utilization because of observation with 6 times per day(100-min orbits).
Since geostationary satellites can give atmospheric motion vector(AMV)s in every 30 minutes, try to estimate SSWs around a typhoon affecting the Korean peninsula using high temporal resolution of low-level AMV data of Geo-Kompsat 2A(GK2A).
Why to use sea surface winds from satellites
GK2A’s 16 channels observations
in every 10 min and full disk area
GK2A AMV in every 30 min and full disk area
Low Earth Orbit(LEO) satellite’s sea surface wind

## Slide 4: Data used to estimate and validate SSWs
Atmospheric Motion Vector(AMV) - Calculated based on the movement of clouds or water vapour observed from GK2A
input channel | Visible(0.63um), Shortwave infra red (3.8um), Infrared (10.5um) : 3 channels
Wind speed | 0 to 100m/s
Wind direction | 0 to 360°
Altitude | 100~1000 hPa
Region | East Asia (3800 X 2400 km )
Temoral resolution | 10 minutes
Spatial resolution | Visible :12 km x 12 km / Infrared: 16 km x 16 km
GK2A’s Atmospheric Motion Vector(AMV)
Typhoon center location by ADT
LEO’s sea surface wind(SSW)
ADT(Advanced Dvorak Technique) - Variable : Typhoon center location with latitude and longitude and in every 10 minutes if a typhoon occurs.
Sea Surface Wind(SSW) - Retrieved from MetOp/ASCAT (Advanced SCATterometer) at 10-m altitude - Spatial resolutions : 25 km, 12.5 km
※ Data period : Summer 2019-2021 (July- September )
Marine buoy’s SSW
BUOY from Korea Hydrographic and Oceanographic Agency (KHOA)
- Observed SSW at open oceans and closed to coasts
For verification

## Slide 5: Input Data: GK2A observation
Full Disk : 1 time in every 10 min
Extended Local Area(ELA) : 3800 X 2400 km, 5 times in every 10 min
LA : 1000 X 1000 km, 5 times in every 10 min
Full Disk
In every 10 min.
ELA
2 min
10 min.
Timeline
LA
2 min
Observation area and frequency of GK2A
GK2A

## Slide 6: Processing to estimate GK2A SSWs
Calculating meam GK2A AMV
Selecting AMVs of VIS, SWIR, IR in 700~1000hPa
Making 2-D arrays with 0.5x0.5km for VIS & 2x2km for SWIR & IR
Calculating mean GK2A AMV with 2x2km
Converting spatial resolution from 0.5km to 2km for VIS
Spatio-temporal
matching btwn mean GK2A AMV & ASCAT SSW
How to select GK2A SSW from mean GK2A AMV data
Only when a typhoon exits in the extended LA(ELA)
Two data of mean GK2A AMV and ASCAT SSW are less than 15 min
Area of ±10 degree from ADT typhoon center
Finally, extracting data from mean GK2A AMV nearest ASCAT SSW

## Slide 7: Method used to estimate GK2A SSWs
Regression
In previous studies of Nonaka et al(2016), wind speed(WS) of Himawari AMV is highly correlated (0.75~0.84) with that of ASCAT SSW:
Comparison between Himawari-8 AMVs and ASCAT SSW within a radius of 1,000 km from the center of TCs from May to December 2015(left: wind speed; right : wind direction) (Nonaka et al. 2016)
The correlation relationship using GK2A AMV and ASCAT wind in this study:
This study applied normalized wind speed btwn AMV and ASCAT because the greater the difference of speeds between GK2A AMV and ASCAT SSW as the the wind speed becomes stronger.
Comparison between GK2A AMVs and ASCAT SSWs from July to September 2020~2021(left: wind speed; right : wind direction)

## Slide 8: Verification of results
Algorithm verification result(2)
Verification using ASCAT SSWs
Verification Period : Typhoon Cases from August to September 2019
Verification results for QI > 0.80 (a) GK2A AMV vs ASCAT (b) GK2A SSW vs ASCAT
Bias : 0.94 m/s  -0.20 m/s RMSE : 2.70 m/s  1.77 m/s
(a)
(b)
GK2A AMV vs ASCAT
GK2A SSW vs ASCAT
※ QI (Quality Index)
: Data quality evaluation based on homogeneity of time and space of vectors and similarity of numerical model winds : With the range of 0 ~1, the closer to 1, the better quality the
vector.
In summary, a distribution of GK2A SSW is more similar to that of ASCAT SSW than GK2A AMV with a little bias and RMSE.

## Slide 9: Verification of results
Verification data : ASCAT SSWs
Verification Period : Typhoon Cases from August to September 2019
Executing verification GK2A AMV vs ASCAT SSW, GK2A SSW vs ASCAT SSW in each class of wind speed
In this study, found that wind speed difference between GK2A and ASCAT SSW for winds with stronger than 15 m/s are decreased largely compared to that of GK2A AMV and ASCAT SSW.
Wind speed (m/s) | Num. | GK2A AMV vs ASCAT SSW |  | GK2A SSW vs ASCAT SSW | 
 |  | Bias | RMSE | Bias | RMSE
0 ~ 5 | 23542 | -0.41 | 1.53 | -0.34 | 1.51
5 ~10 | 84506 | 0.75 | 1.87 | 0.11 | 1.63
10 ~ 15 | 53615 | 2.70 | 3.37 | 0.45 | 1.98
15 ~ 20 | 20178 | 5.14 | 5.68 | 0.61 | 2.27
20 ~ 25 | 2977 | 8.27 | 8.70 | 1.04 | 2.84
25 ~ 30 | 225 | 10.74 | 10.91 | 0.24 | 1.74
Algorithm verification result(2)
☞ For strong tropical cyclones (> 15 m/s), GK2A SSW data is more useful to analyze storms.

## Slide 10: Verification of results
Lingring
Tapah
Krosa
Lekima
Francisco
Francisco Bias: 0.44, RMSE: 1.59
Lekima Bias: 0.46, RMSE: 2.08
Krosa Bias: 0.54, RMSE: 2.00
Lingling Bias: 0.36, RMSE: 1.19
Tapah Bias: -1.43, RMSE: 4.70
Verification results for typhon cases in 2019
In summary for typhoons affecting to the Korean peninsula,
Bias: -1.43~0.54
RMSE: 1.19~4.70

## Slide 11: Results: case study
GK2A SSW
2019.09.07. 00:00 ~ 07:00 UTC
Typhoon “Lingling” moved northward with difficulty in predicting the typohoon moving course, and there was warning information about many damages of the Korean peninsula due to extremly strong winds
No observations of microwave low earth orbit(LEO) satellites passing over the typhoon radius after 12:00 UTC on September 6, 2019 when the Korean peninsula was affected in the typhoon's gale radius,  Difficulty in acquiring sea surface wind information
Lingling (2019)
Result from comparison with GK2A SSW and BUOY SSW observed at the west and south seas of the Korean peninsula:
Bias= -0.39 m/s,
RMSE=1.82 m/s

## Slide 12: Results: case study
Tapha(2019)
Combination of GK2A and ASCAT SSWs can provide wind information of the lower layer of a typhoon in a wide area
Limitation : Accuracy of GK2A SSW can be decreased at night due to no information of AMV of visible channel
GK2A SSW + ASCAT SSW
2019.09.22. 22 KST (Night time)
SWIR AMV based SSW (Night time)
VIS AMV based SSW (Day time)

## Slide 13: Results: case study
GK2A SSW
METOP-B/ASCAT SSW
Krosa (2019)
GK2A + ASCAT SSW
2019.08.11. 23:00 ~ 08.12. 09:00UTC

## Slide 14: Validation of GK2A ASWind accuracy
2022 Verification
Speed (m/s) | N | GK-2A Low-level AMV |  | GK-2A ASWind |  | JMA method ASWind | 
 |  | Bias | RMSD | Bias | RMSD | Bias | RMSD
0 – 5 | 28249 | -0.50 | 1.54 | -0.44 | 1.51 | -1.48 | 2.06
5 – 10 | 146743 | 0.79 | 1.61 | 0.20 | 1.33 | -0.98 | 1.64
10 – 15 | 98683 | 2.43 | 3.00 | 0.09 | 1.69 | -0.54 | 1.78
15 – 20 | 35282 | 4.45 | 4.76 | -0.06 | 1.53 | 0.41 | 1.63
20 – 25 | 7325 | 7.11 | 7.34 | -0.29 | 1.72 | 1.88 | 2.56
25 – 30 | 739 | 9.27 | 9.38 | -0.86 | 1.51 | 3.04 | 3.32
Years | Typhoon name | Formed | Dissipated | Maximum wind speed around center(m/s) | Landfall
2022 | AERE | 7. 1. 09KST | 7. 5. 03KST | 20 | X
 | SONGDA | 7. 28. 21KST | 8. 1. 03KST | 20 | X
 | TRASES | 7. 31. 12KST | 8. 1. 09KST | 18 | X
 | HINNAMNOR | 8. 28. 21KST | 9. 6. 21KST | 55 | O
 | NANMADOL | 9. 14. 03KST | 9. 20. 09KST | 55 | X

## Slide 15: Results: case study
MetOp/ASCAT SSW
GK2A SSW
Nanmadol(2022)

## Slide 16: Validation of GK2A ASWind accuracy
AMV → ASWind
Regression

## Slide 17: Conclusion and summary
This study aimed to develop a technique for estimating sea surface wind(SSW) information using atmospheric motion vector(AMV) data from the Geo-Kompsat-2A (GK2A), which has high temporal(30 min) and spatial resolution(16x16km).
For quantitative verification between GK2A SSW and ASCAT (or BUOY) SSW - For GK2A vs ASCAT, Bias = -0.20 m/s, RMSE = 1.77 m/s
- For GK2A vs BUOY, Bias = -0.39 m/s, RMSE = 1.89 m/s - Reducting wind speed difference between GK2A SSW and ASCAT SSW over 15 m/s
For qualitative Verification - GK2A SSW can provide information of the low-level wind of a typhoon in a wide area if GK2A SSW data combines to ASCAT SSW
- In case of a typhoon separated from the upper and lower levels,
GK2A SSW can help to analyze the typhoon and its center.
Some limitations
- Since GK2A AMV is calculated by tracking the movement of the cloud top, it is impossible to obtain
lower layer vector data in areas if clouds are thick or upper layer clouds exist. - Accuracy and density of data can be decreased at night due to no information of
AMV of visible channel.

## Slide 18: references
Nonaka , K., K. Shimoji , and Y. Igarashi, 2019: Utilization of Estimated Sea Surface Wind Data Based on Himawari-8/9 Low-level AMVs for Tropical Cyclone Analysis
Nonaka , K., K. Shimoji , and K. Kato, 2016: Estimation of The Sea Surface Wind in The Vicinity of Typhoon using Himawari-8 Low-Level AMVs . Proc. of 13th International Winds Workshop.
Franklin, JL, ML Black, and K. Valde, 2003: GPS Dropsonde Wind Profiles in Hurricanes and Their Operational Implications. Wea. Forecasting, 18, 32-43.
Holmlund, K., 1998: The utilization of statistical properties of satellite-derived atmospheric motion vectors to derive quality indicators. Wea. Forecasting, 13, 1093-1104 .

## Slide 19: Thank you for your attention!